## Slide 1
Tomingley Gold Project
7 Years On…
September 2013
David Meates
Ian Chalmers
Terry Ransted
Notes: This is an update to the last technical presentation we did at a M&W 7 years ago and as seen from the photo, 12 years on from discovery things are starting to develop nicely… A couple of names to mention who aren’t here today but Ian Chalmers our MD and Terry Ransted the chief geo both remain closely involved with the project.

## Slide 2
Rimas Kairaitis (Alkane-YTC Resources Ltd)
Dr Anthony Crawford (A & A Crawford Geological Research Consultants)
Peter Schaubs (CSIRO)
Acknowledgements

## Slide 3
Significant orogenic gold in Ordovician volcanics of Eastern Lachlan
Global Resource (excl Caloma Two): 12.6Mt @ 2.0g/t Au (811,700oz)
7 year mine life to produce 50-60,000ozpa at 1Mpta
Development approval February 2013, first production early 2014
Caloma Two resource calc. underway - Significant intercepts inc:
  70m grading 1.89g/t gold from 176m (PE788)
  9m grading 110g/t gold from 194m
  including 1m grading 822g/t gold (PE873)
Summary

## Slide 4
Background

## Slide 5
Newell Highway
Tomingley Village
Peak Hill Gold Mine
0.7Moz
Myalls United Mine
60,000oz prd.
Wyoming Three
50,000oz
Wyoming One
390,000oz
Caloma Two
tbc
Caloma
370,000oz
Background
Notes: TGP aerial photo with sites of interest

## Slide 6
2001 Tenements acquired from Compass Resources and Golden Cross Resources through royalty from production.
2004 Wyoming deposits open cut resources defined.
2005 Preliminary feasibility study on Wyoming deposits was not positive.
Wyoming One underground resource subsequently defined.
2009 Caloma open cut resource defined.
2011 Positive definitive feasibility study completed.
EA with development approval sought.
2013 Mining lease granted, construction commences.
Caloma Two resource definition underway.
Background
Notes: Wyo Resource Summary

## Slide 7
Infrastructure:
  water => 45km pipeline
  power (State Grid) => 20km 66Kv power line
  roads => primary & secondary access
Skilled local workforce
  population base of 150,000 within 120km diameter area
  No FIFO
Site layout
Background

## Slide 8
Geological Setting
Caloma Two initial RC drilling
July 2010

## Slide 9: Structural Divisions of the Lachlan Orogen
Geological Setting

## Slide 10: Macquarie Arc Major Deposits (Modern)
Bathurst
Wellington
Orange
Dubbo
Forbes
Parkes
Molong
Volcanic
Belt
Rockley
Gulgong
Volcanic
Belt
Junee
Narromine
Volcanic
Belt
Northparkes
1.5M oz
Cowal
6M oz
Gidginbung
0.7M oz
Peak Hill
0.7M oz
Cadia Valley
44M oz
Monzonitic intrusions
Ordovician arc volcanics
Fifield complexes
Younger granites
Tomingley
0.8M oz
Geological Setting

## Slide 11: TGP Tenements Regional Geology
Late Devonian sediments
Early Devonian granites
Late Silurian to Mid Devonian volcanics
and sediments
Ordovician to Silurian sediments
Ordovician volcanic complexes
Northparkes
Mingelo
Volcanics
TGP
PHGM

## Slide 12: Parkes - Narromine Regional Aeromagnetics Merged Alkane detailed with DMR regional data
Tomingley
Peak Hill
LTZ
Parkes Thrust
North Parkes

## Slide 13
Local Geology
Ore zones hosted within or along margins of feldspar phyric monzodiorite sills
Geology concealed by variably thick magnetic overburden
Deep weathering profile
East-west compression followed by dextral wrenching
Extensional post-mineralisation dyking
369,000oz @ 2.1g/t Au
Resource to be calculated
50,000oz @ 1.9g/t Au
392,000oz @ 1.9g/t Au
392,000oz @ 1.9g/t Au
Notes: Wyoming geology summary

## Slide 14
Arsenopyrite in Caloma core
Ore Genesis

## Slide 15
Multiphase alteration assemblage: sericite – ankerite – albite – chlorite – quartz – (fuchsite)
Weak zoning of carbonate spotting (ankerite)
Mineralisation: pyrite – arsenopyrite (up to 5% As) trace: sphalerite, chalcopyrite, pyrrhotite
Gold forming within brittle fractures within quartz veins and pyrite
2 significant deformation events, E-W compression and subsequent dextral transpression
Middle Devonian Tabberabberan Orogeny likely
Ore Genesis
Apy

## Slide 16
Discovery History
Myalls United Lode 1883 - 1912
Notes: Wyo Resource Summary

## Slide 17
10m @ 0.6g/t Au
3300ppm As to EOH
16m @ 1.7g/t Au,
500ppm As
11m @ 1.0g/t Au,
1800ppm As
4m @ 0.8g/t Au,
500ppm As to EOH
14m @ 3.4g/t Au
2100ppm As to EOH
76m @ 9.1g/t Au,
2.3% As
17m @ 9.2g/t Au,
500ppm As
8m @ 1.4g/t Au, 900ppm As + 6m @ 1.3g/t Au, 3000ppm As to EOH
3m@ 2.4g/t Au, 3200ppm As to EOH
17m@ 2.5g/t Au, 600ppm As
9m@ 6.9g/t Au, 500ppm As to EOH
9m@ 3.1g/t Au, 900ppm As to EOH
70m@ 1.9g/t Au, 3000ppm As
9m@ 110g/t Au, 800ppm As
Discovery History
Compass drilling
Hanging Wall Zone
Total resource definition – 2,306 drill holes for 231,504 metres.
Expenditure (incl feasibility and EA) $35 million or $43/ounce (Caloma Two pending)

## Slide 18
Discovery History
Detailed magnetic imagery
Angled pattern air-core drilling – mapping and geochemistry
Early stage diamond core drilling
Persistence – poddy nature of these styled deposits
Exploration Methodology
Notes: Wyo drilling history

## Slide 19: Conclusions
Significant gold mineralisation (~1Mo) defined as a orogenic gold style within Ordovician volcanics of the Eastern Lachlan Fold Belt.
Main exploration tools:
  High resolution aeromagnetics
  Air-core drilling
  Follow up drilling (RC, DD)
Dextral wrenching a significant structural control
Ongoing research of characterising the sulphide mineralisation, inc. S isotopes, K/Ar dating is in progress (Alex Cherry, Honours, UNSW)